## Slide 1: Autonomous System to Establish Reference Direction for Large Ground-Based Antennas

## Slide 2: Boresighting
Aligning an antenna with a target
  Tight accuracies
  Slow process (2 days)
  Labor intensive
  Long distances between required measurements
  Expensive equipment

## Slide 3: Key Success Measurements

## Slide 4: Our Solution

## Slide 5: Step by Step Process
Set up base station
Initiate GPS and leveling procedure
Place mobile station
Align gimbal with the mobile station
Input GPS coordinates of the target

## Slide 6: Place Mobile Station
Place mobile station about 100m from antenna
Place in clearing
  Avoid multipath
  taller is better
Turn on device
Check that blue LED is on
Automatically begins survey-in

## Slide 7: Rover Setup
Takes 20 seconds to set up rover
Once powered, the rover automatically starts surveying-in and will send RTK correctional data to base station once they survey-in is finished

## Slide 8: North Finding
RTK GPS system
Located in both units
Finds relative position between both units
  Survey in
  RTK fix
Calculates north vector

## Slide 9: Interfacing and Testing
Pi interacts with Ublox via Serial (NMEA protocol, mostly proprietary UBX)
Survey-In, High Precision Position, RTK status, relative Position, Message Enable.
Surveying in at Y
Surveying in/Surveying targets at Park
Timing variability

## Slide 10: Testing and Validation
Time: Variable but typically 2 minutes
Determine location with centimeter accuracy
0.014° accuracy

## Slide 11: Testing and Validation
RTK Solution measured accuracy: 2.6 cm
  Predicted of 1.732 cm (in 3 Dimensions)
Time to establish an RTK Fix: 1-5 minutes
  Highly Variable (atmosphere, multipath, baseline length, satellite visibility)
Survey-in Accuracy:
No observable correlation between survey-in time and RTK fix time
    1.4197m in 1 min
    1m in 13 mins,
    .54m in 42 mins,
    .55m in 97 mins (on Y mountain, bad multipath)

## Slide 12: Setup Base Station
Setup Tripod
  5° of level
Connect to power
Turn on system
Follow UI

## Slide 13: Base Station Setup
Takes roughly 1 minute to set up base station

## Slide 14: Align Gimbal and Mobile Station
Creates a reference location for the gimbal
Manually established using a scope camera system

## Slide 15: The Gimbal
Allows alignment of the entire
system and pointing at the final target
Two axis of rotation
Ramping function
Encoders
Accuracy: 0.002° per step
Rotation Speed: 1 RPM

## Slide 16: Design and Testing

## Slide 17: Additional Testing

## Slide 18: Manually Establishing The Baseline
Keypad controls gimbal
Visual display allows user to
establish the baseline
Scope is aligned with the U-blox
antenna
1” X 1” target easily found at 100
Meters
Accuracy: 0.01°

## Slide 19: Baseline Setup
Align orientation of gimbal with baseline
This is accomplished by pointing the scope at the rover’s GPS antenna
Variable gimbal speed allows user to accurately point at rover

## Slide 20: Input Pointing GPS Coordinates
UI navigation and target GPS coordinates are entered via keypad on the handheld

## Slide 21: Level The Gimbal
Triple-axis accelerometer
The gimbal system pans in 45° intervals allowing the accelerometer to take readings at different locations
Self-levels
Rotates again to validate how level the system is

## Slide 22: Testing and Validation
Noise verified to ≤ 1 LSB
17-bit ADC
Experimentally verified average offset from level of 0.012° over 10 trials

## Slide 23: Self-Calibration

## Slide 24: Full Test

## Slide 25: Cost
Gimbal costs not included in final cost of the system
Key Components
  U-blox
  Accelerometer
  Simmons 3-9 power scope
  7” screen
  Raspberry Pi
Total Cost: $968

## Slide 26: Deliverables
Full system
Design Package
  Setup Procedure
  Code
  CAD models
  Circuitry design
  Testing and validation
procedures and data
Documented design process performed by the team

## Slide 27: Recommendations
Object recognition for establishing baseline
Encoders
  Self Leveling
Additional Testing
Replace 3D prints

## Slide 28: Results